## Slide 1: Rapid Estimation of Mission Feasibility

## Slide 2: Overview of method
Estimation of average edge length
Estimation of total distance
Estimation of mission duration
Validation tests of method

## Slide 3: Average Edge Length Estimation

## Slide 4: Start with the Search Area. Assume it has some characteristic length, L, where L is the length of one Side. 360 miles
Helpful knowledge for maps: Each degree of Latitude or Longitude is usually about 70 miles. So, roughly, a 1 arc-minute is about a mile

## Slide 5: Count the Number of POINTS IN the area
This can be number of mission goals, grid size, etc
  It should represent the distance between edges, where each edge is an independent direction to a target.
  Treat clusters of targets as one target
  Let’s assume high, or 36 for us.
  The number of points per edge is, assuming points are spread roughly evenly over the search area, the square-root of the number of points. Or in this example, 6 on each edge.

## Slide 6: The Average edge length is then simply The Edge length Divided by the number of points per edge. 360 miles/6 = 60 miles per edge

## Slide 7: Estimation of Total Distance is the sum of edges
Total distance is average distance per edge multiplied by number of edges
  36 edges *60 miles/edge = 2000 to 2500 miles
  If we look at the math, it is
  N * L/N^0.5 = L * N^0.5
  Where L is side length, N is number of goals.

## Slide 8: Estimation of mission duration is Straightforward
Take average speed, say 50 mph, and use this to estimate mission time. For 2200 miles, this is about 45 hours.
The formula: Time = N^0.5 * L / V
Where N is number of goals, L is side length, V is velocity

## Slide 9: Does this work?
(Code is from: https://www.mathworks.com/help/optim/ug/traveling-salesman-problem-based.html)

## Slide 10: THANK YOU
Sean Brenan
Penn State
sbrennan@psu.edu